## Slide 1: Quantum detector tomography of a nanophotonic-amplifier-based single photon detector
Elina Sendonaris
esendona@caltech.edu
Quantum Nanophotonics 2025
24/3/25

## Slide 2
Quantum imaging and sensing
Quantum photonics
Quantum information processing
J. Yin, et al, Nature 582 (501-503) (2020)
Challenges: scalability, nonlinearity
Quantum communication
H.-S. Zhong, et al., Science 370 6523 (2020)
G. Lemos, et al., Nature 512 (409–412) (2014)

## Slide 3: Lithium niobate integrated quantum photonics
R. Nehra, et al., Science, 2022 37 (2022)
D. Zhu, et al., Optica, 13 2 (2021)
Benefits:
Strong χ(2) optical nonlinearity
Wealth of linear and nonlinear components
Scalability
G. H. Y. Li, et al., Light: Science & Applications 12 (2023)

## Slide 4: Optical parametric amplifiers (OPAs)
Degenerate OPA
Quadrature squeezing
Vacuum
Squeezed vacuum

## Slide 5: Integrated thin-film lithium niobate OPAs
Dispersion engineering for ultrashort pulse operation and high gain
L. Ledezma et al., Optica 9 3 (2022)
High spatial mode confinement
J. Willliams et al., Nanophotonics 13 (2024)

## Slide 6
Necessary for quantum communication and computation
Photon detection in nanophotonics
Integrate a superconducting detector on-chip
Outcouple from chip to detector
A. Sayem, et al., Applied Phys. Lett., 116 151102 (2020)
Speed limited by reset time of physical process
Entire chip must be in cryostat
J. M. Arrazola, et al., Nature 591 54-60 (2021)
Issues: High outcoupling loss

## Slide 7: Photon detection using an optical parametric amplifier
OPA detector: OPA + macroscopic detector
OPA amplifies signal to macroscopic levels
Thresholding to identify a photon (click detector)

## Slide 8: Why integrated OPAs for photon detection?
Ultrafast (THz)
Room-temperature
Wide wavelength range
High gain
Resistant to out-coupling loss
Integrated

## Slide 9: Photon detection using an optical parametric amplifier – photodetector
Photodetector
Gaussian operation
OPA in linear regime
Not sufficient for universal quantum computation

## Slide 10: Quantum detector tomography
Obtain POVM through inversion of:
Measurement results
Probe state
POVM
Integrated periodically-poled lithium niobate OPA
18 GHz fast photodetector
100 fs pump pulses

## Slide 11: OPAD performance
Want:
High photon detection efficiency
Low dark count rate

## Slide 12: OPAD discrete variable performance
Start with a Bell state in the Fock basis
High fidelity of other mode with single photon conditioned on click
Non-Gaussianity remains

## Slide 13: Photon detection using an optical parametric amplifier – pump homodyne
QND measurement using homodyne on depleted pump:
R. Yanagimoto et al., PRX Quantum 4, 010333 (2023)
Large nonlinearity-to-loss ratio (g/κ) leads to pump-signal entanglement
Homodyne measurement of pump projects signal onto squeezed Fock basis

## Slide 14: Photon detection using an optical parametric amplifier – pump homodyne
QND measurement using homodyne on depleted pump:
R. Yanagimoto et al., PRX Quantum 4, 010333 (2023)
Pump Homodyne Detection

## Slide 15: Schrodinger’s cat through pump homodyne OPAD
With g/κ ~ ¼, non-Gaussian behavior arises
Fidelity with photon-subtracted squeezed-state: 0.96
Our g/κ: 0.0033
  Multimode effects
  Material loss
g/κ ~ 0.01 achieved on TFLN (J. Lu et al. Optica 7, 1654–1659 (2020))
  Lower sidewall roughness
  Shorter pulses: g ∝ 1/

## Slide 16: Recap of completed work
Designed and implemented OPA-based single-photon detection system
Integrated, room-temperature, ultrafast operation, no non-Gaussianity
26.5% efficiency for 2.2% dark count rate
Next steps:
Non-Gaussian operation with higher g/κ and pump homodyne
E. Sendonaris* and J. Williams* et al., arXiv:2410.18397 (2024)
Email: esendona@caltech.edu

## Slide 17: Thank you!
Thank you to everyone in the Nonlinear Photonics Lab, especially James Williams, Thomas Zacharias, Robert Gray, Ryoto Sekine, Luis Ledezma, and Alireza Marandi

## Slide 19: Reconstructed POVM
Theoretical POVM:
Fidelity between theoretical and experimental POVMs of 0.72
E. Sendonaris* and J. Williams* et al., arXiv:2410.18397 (2024)